## Slide 1
Central Tracking: Cylindrical µRWELL @ TU
Layers
Vertex
Layers
Cylindrical simulation overview
  TU graduate student Nick Lukow has taken over the bulk of the simulation work.
  Investigate central tracking performance with silicon vertex detector and cylindrical layers in a 1.5 T field.
  Silicon vertex detector
    4 layers each with X-Y pixel resolution of 20m - 20m
Detectors
  Silicon vertex detector
    4 layers each with X-Y pixel resolution of 20m - 20m
  Cylindrical Barrel Tracker
    Consists of six 2m long cylindrical layers covering radii from 22.5 cm-77.5 cm
    For each layer
      One hit point with resolution of ~100 (longitudinal) x ~100 (transverse)
      Detector material ,
      Additional 15 mm of ArCO2 implemented as drift gap

## Slide 2
Central Tracking: Cylindrical µRWELL @ TU
Comparison to TPC performance
  Implemented a TPC into simulation based on sPHENIX TPC
  TPC parameters
    Radial length: 80 cm
    Dispersion (longitudinal, transverse)
      (1 , 15 )
    Resolution (longitudinal, transverse)
      (500 , 200 )
  Transverse dispersion and resolution need to be updated to match sPHENIX transverse (dispersion, resolution) beam test results (40 , 90 )
    We do find particular sensitivity to the transverse dispersion
  Material scan shows the TPC having less material overall than the current 6 cylindrical barrel.

## Slide 3
Central Tracking: Cylindrical µRWELL @ TU
Comparison of and TPC performance
  Performance of cylindrical barrel was done using three (longitudinal, transverse) spatial resolution values
    (100 m, 100 m), (150 m, 150 m), and (200 m, 200 m)
  Using the stated detector simulation conditions, 6 GeV electrons were simulated in a 1.5 T magnetic field
  Theta resolution vs. theta
    appears to have a better angular resolution than the TPC, particularly at smaller angle (.
  Momentum resolution vs. theta
    TPC appears to have a better momentum resolution at small angle ().
    Momentum resolution of the with resolution (100 m, 100 m) becomes comparable to the TPC at moderate angles ()
Results include the
vertex detector

## Slide 4
Central Tracking: Cylindrical µRWELL @ TU
Recent Progress
  We have had several conversations with DIRC representatives from the PID consortium to better understand their tracking needs.
  Added dead material representing the DIRC
    Radial length: 80 cm, thickness 6 cm,
  Track residuals at the DIRC show large sensitivity to TPC transverse dispersion.
  Begun investigating tracking performance with additional layer surrounding
    The DIRC in both cylindrical barrel and TPC configurations
    Only the TPC
Next steps for simulation work
    Include multiple hit points and (mini-drift) mode
    Optimize number of cylindrical layers and their spacing
    Implement FIT support structure
  TPC
    Update simulations using measured sPHENIX transverse resolution
    Investigate performance with layer surrounding TPC
  DIRC
    Continue discussions with PID consortium (DIRC) to understand needed tracking performance
    Implement realistic budget material
Track residuals from TPC
at DIRC
(%)
Electrons
DIRC

## Slide 5
End Cap Tracking: Commercial GEMs @ TU
GEM CCD Scanner
  Continues to serve the MPGD community
  Recently completed or upcoming scans
    foil (completed last summer)
    Low Temperature Co-fired Ceramic GEM (to start soon)
  Recently (this past summer) we completed scans of an FIT foil that was deemed “bad” by CERN.
Foil Scan
  Investigate hole (well) pitch and diameter uniformity of a .
  FIT sent us a bare foil not mounted to a substrate that CERN determined to be “bad”.
  Measurements of the pitch and outer hole (well) diameters were found to be uniform.
    Pitch:
    Outer well diameter deviation: